## Slide 1: Cell Programming Tutorial
Jeff Derby, Senior Technical Staff Member, IBM Corporation

## Slide 2: Outline
Program structure – PPE code and SPE code
SIMD and vectorization
Communication between processing elements – DMA, mailboxes
Programming models
Code example

## Slide 3: PPE Code and SPE Code
PPE code – Linux processes
  a Linux process can initiate one or more “SPE threads”
SPE code – “local” SPE executables (“SPE threads”)
  SPE executables are packaged inside PPE executable files
An SPE thread:
  is initiated by a task running on the PPE
  is associated with the initiating task on the PPE
  runs asynchronously from initiating task
  has a unique identifier known to both the SPE thread and the initiating task
  completes at return from main in the SPE code
An SPE group:
  a collection of SPE threads that share scheduling attributes
  there is a default group with default attributes
  each SPE thread belongs to exactly one SPE group

## Slide 4: Code Sample
PPE code:
SPE code:
(but “printf” from SPE only in the simulator environment …)
#include <stdio.h>
#include <libspe.h>
extern spe_program_handle_t hello_spu;
int main(void)
{
speid_t speid;
int status;
speid = spe_create_thread (0, &hello_spu, NULL, NULL, -1, 0);
spe_wait(speid, &status, 1);
return 0;
#include <stdio.h>
#include <cbe_mfc.h>
#include <spu_mfcio.h>
int main(speid_t speid, unsigned long long argp, unsigned long long envp)
{
printf("Hello world!\n");
return 0;
}

## Slide 5: SIMD Architecture
SIMD = “single-instruction multiple-data”
SIMD exploits data-level parallelism
  a single instruction can apply the same operation to multiple data elements in parallel
SIMD units employ “vector registers”
  each register holds multiple data elements
SIMD is pervasive in the BE
  PPE includes VMX (SIMD extensions to PPC architecture)
  SPE is a native SIMD architecture (VMX-like)
SIMD in VMX and SPE
  128bit-wide datapath
  128bit-wide registers
  4-wide fullwords, 8-wide halfwords, 16-wide bytes
  SPE includes support for 2-wide doublewords

## Slide 6: A SIMD Instruction Example
Example is a 4-wide add
  each of the 4 elements in reg VA is added to the corresponding element in reg VB
  the 4 results are placed in the appropriate slots in reg VC

## Slide 7: SIMD “Cross-Element” Instructions
VMX and SPE architectures include “cross-element” instructions
  shifts and rotates
  permutes / shuffles
Permute / Shuffle
  selects bytes from two source registers and places selected bytes in a target register
  byte selection and placement controlled by a “control vector” in a third source register
  extremely useful for reorganizing data in the vector register file

## Slide 8: Shuffle / Permute – A Simple Example
Bytes selected from regs VA and VB based on byte entries in control vector VC
Control vector entries are indices of bytes in the 32-byte concatenation of VA and VB
Operation is purely byte oriented
SPE has extended forms of the shuffle / permute operation

## Slide 9: SIMD Programming
“Native SIMD” programming
  algorithm vectorized by the programmer
  coding in high-level language (e.g. C, C++) using intrinsics
  intrinsics provide access to SIMD assembler instructions
    e.g. c = spu_add(a,b)  add vc,va,vb
“Traditional” programming
  algorithm coded “normally” in scalar form
  compiler does auto-vectorization
  but auto-vectorization capabilities remain limited

## Slide 10: C/C++ Extensions to Support SIMD
Vector datatypes
  e.g. “vector float”, “vector signed short”, “vector unsigned int”, …
  SIMD width per datatype is implicit in vector datatype definition
  vectors aligned on quadword (16B) boundaries
  casts from one vector type to another in the usual way
  casts between vector and scalar datatypes not permitted
Vector pointers
  e.g. “vector float *p”
  p+1 points to the next vector (16B) after that pointed to by p
  casts between scalar and vector pointer types
Access to SIMD instructions is via intrinsic functions
  similar intrinsics for both SPU and VMX
  translation from function to instruction dependent on datatype of arguments
  e.g. spu_add(a,b) can translate to a floating add, a signed or unsigned int add, a signed or unsigned short add, etc.

## Slide 11: Vectorization
For any given algorithm, vectorization can usually be applied in several different ways
Example: 4-dim. linear transformation (4x4 matrix times a 4-vector) in a 4-wide SIMD
Consider two possible approaches:
  dot product: each row times the vector
  sum of vectors: each column times a vector element
Performance of different approaches can be VERY different

## Slide 12: Vectorization Example – Dot-Product Approach
Assume:
  each row of the matrix is in a vector register
  the x-vector is in a vector register
  the y-vector is placed in a vector register
Process – for each element in the result vector:
  multiply the row register by the x-vector register
  perform vector reduction on the product (sum the 4 terms in the product register)
  place the result of the reduction in the appropriate slot in the result vector register

## Slide 13: Vectorization Example – Sum-of-Vectors Approach
Assume:
  each column of the matrix is in a vector register
  the x-vector is in a vector register
  the y-vector is placed in a vector register (initialized to zero)
Process – for each element in the input vector:
  copy the element into all four slots of a register (“splat”)
  multiply the column register by the register with the “splatted” element and add to the result register

## Slide 14: Vectorization Trade-offs
Choice of vectorization technique will depend on many factors, including:
  organization of data arrays
  what is available in the instruction-set architecture
  opportunities for instruction-level parallelism
  opportunities for loop unrolling and software pipelining
  nature of dependencies between operations
  pipeline latencies

## Slide 15: Communication Mechanisms
Mailboxes
  between PPE and SPEs
DMA
  between PPE and SPEs
  between one SPE and another

## Slide 16: Programming Models
One focus is on how an application can be partitioned across the processing elements
  PPE, SPEs
Partitioning involves consideration of and trade-offs among:
  processing load
  program structure
  data flow
  data and code movement via DMA
  loading of bus and bus attachments
  desired performance
Several models:
  “PPE-centric” vs. “SPE-centric”
  “data-serial” vs. “data-parallel”
  others …

## Slide 17: “PPE-Centric” & “SPE-Centric” Models
“PPE-Centric”:
  an offload model
  main line application code runs in PPC core
  individual functions extracted and offloaded to SPEs
  SPUs wait to be given work by the PPC core
“SPE-Centric”:
  most of the application code distributed among SPEs
  PPC core runs little more than a resource manager for the SPEs (e.g. maintaining in main memory control blocks with work lists for the SPEs)
  SPE fetches next work item (what function to execute, pointer to data, etc.) from main memory (or its own memory) when it completes current work item

## Slide 18: A Pipelined Approach
Data-serial
Example: three function groups, so three SPEs
Dataflow is unidirectional
Synchronization is important
  time spent in each function group should be about the same
  but may complicate tuning and optimization of code
Main data movement is SPE-to-SPE
  can be push or pull

## Slide 19: A Data-Partitioned Approach
Data-parallel
Example: data blocks partitioned into three sub-blocks, so three SPEs
May require coordination among SPEs between functions
  e.g. if there is interaction between data sub-blocks
Essentially all data movement is SPE-to main memory or main memory-to-SPE

## Slide 20: Software Management of SPE Memory
An SPE has load/store & instruction-fetch access only to its local store
  Movement of data and code into and out of SPE local store is via DMA
SPE local store is a limited resource
SPE local store is (in general) explicitly managed by the programmer

## Slide 21: Overlapping DMA and Computation
DMA transactions see latency in addition to transfer time
  e.g. SPE DMA get from main memory may see a 475-cycle latency
Double (or multiple) buffering of data can hide DMA latencies under computation, e.g. the following is done simultaneously:
  process current input buffer and write output to current output buffer in SPE LS
  DMA next input buffer from main memory
  DMA previous output buffer to main memory
  requires blocking of inner loops
Trade-offs because SPE LS is relatively small
  double buffering consumes more LS
  single buffering has a performance impact due to DMA latency

## Slide 22: A Code Example – Complex Multiplication
In general, the multiplication of two complex numbers is represented by
Or, in code form:
/* Given two input arrays with interleaved real and imaginary parts */
float input1[2N], input2[2N], output[2N];
for (int i=0;i<N;i+=2) {
float ac = input1[i]*input2[i];
float bd = input1[i+1]*input2[i+1];
output[i] = (ac – bd);
/*optimized version of (ad+bc) to get rid of a multiply*/
/* (a+b) * (c+d) –ac – bd = ac + ad + bc + bd –ac –bd = ad + bc */
output[i+1] = (input1[i]+input1[i+1])*(input2[i]+input2[i+1]) - ac - bd;
}

## Slide 23: Complex Multiplication SPE - Shuffle Vectors
a1
b1
a2
b2
A1
a3
b3
a4
b4
A2
c1
d1
c2
d2
B1
c3
d3
c4
d4
B2
0-3
8-11
16-19
24-27
I P
4-7
12-15
20-23
28-31
Q P
Input
Shuffle patterns
I1 = spu_shuffle(A1, A2, I_Perm_Vector);
a1
b1
a2
b2
A1
a3
b3
a4
b4
A2
0-3
8-11
16-19
24-27
I P
a1
a2
a3
a4
I1
I2 = spu_shuffle(B1, B2, I_Perm_Vector);
c1
c2
c3
c4
I2
Q1 = spu_shuffle(A1, A2, Q_Perm_Vector);
a1
b1
a2
b2
A1
a3
b3
a4
b4
A2
b1
b2
b3
b4
Q1
d1
d2
d3
d4
Q2
4-7
12-15
20-23
28-31
Q P
Q2 = spu_shuffle(B1, B2, Q_Perm_Vector);
Z1
Z2
By analogy
By analogy
Z3
Z4
W1
W2
W3
W4

## Slide 24: Complex Multiplication
A1 = spu_nmsub(Q1, Q2, v_zero);
A2 = spu_madd(Q1, I2, v_zero);
Q1 = spu_madd(I1, Q2, A2);
I1 = spu_madd(I1, I2, A1);
b1
b2
b3
b4
Q1
d1
d2
d3
d4
Q2
0
0
0
0
Z
*
-
-(b1*d1)
A1
-(b2*d2)
-(b3*d3)
-(b4*d4)
b1
b2
b3
b4
Q1
*
+
b1*c1
A2
b2*c2
b3*c3
b4*d4
c1
c2
c3
c4
I2
0
0
0
0
Z
*
+
a1*d1+
b1*c1
Q1
a1
a2
a3
a4
I1
d1
d2
d3
d4
Q2
b1*c1
A2
b2*c2
b3*c3
b4*d4
a2*d2+
b2*c2
a3*d3+
b3*c3
a4*d4+
b4*c4
*
+
a1*c1-
b1*d1
I1
a1
a2
a3
a4
I1
a2*c2-
b2*d2
a3*c3-
b3*d3
a4*c4-
b4*d4
c1
c2
c3
c4
I2
-(b1*d1)
A1
-(b2*d2)
-(b3*d3)
-(b4*d4)

## Slide 25: Complex Multiplication – Shuffle Back
D1 = spu_shuffle(I1, Q1, vcvmrgh);
D2 = spu_shuffle(I1, Q1, vcvmrgl);
a1*d1+
b1*c1
Q1
a2*d2+
b2*c2
a3*d3+
b3*c3
a4*d4+
b4*c4
a1*c1-
b1*d1
I1
a2*c2-
b2*d2
a3*c3-
b3*d3
a4*c4-
b4*d4
0-3
16-19
4-7
20-23
V1
8-11
24-27
12-15
28-31
V2
Shuffle patterns
Results
a1*d1+
b1*c1
Q1
a2*d2+
b2*c2
a3*d3+
b3*c3
a4*d4+
b4*c4
a1*c1-
b1*d1
I1
a2*c2-
b2*d2
a3*c3-
b3*d3
a4*c4-
b4*d4
0-3
16-19
4-7
20-23
V1
D1
a1*c1-
b1*d1
a1*d1+
b1*c1
a2*c2-
b2*d2
a2*d2+
b2*c2
a1*d1+
b1*c1
Q1
a2*d2+
b2*c2
a3*d3+
b3*c3
a4*d4+
b4*c4
a1*c1-
b1*d1
I1
a2*c2-
b2*d2
a3*c3-
b3*d3
a4*c4-
b4*d4
D1
8-11
24-27
12-15
28-31
V2
a3*c3-
b3*d3
a3*d3+
b3*c3
a4*c4-
b4*d4
a4*d4+
b4*c4

## Slide 26: Complex Multiplication – SPE - Summary
vector float A1, A2, B1, B2, I1, I2, Q1, Q2, D1, D2; /* in-phase (real), quadrature (imag), temp, and output vectors*/
vector float v_zero = (vector float)(0,0,0,0);
vector unsigned char I_Perm_Vector = (vector unsigned char)(0,1,2,3,8,9,10,11,16,17,18,19,24,25,26,27);
vector unsigned char Q_Perm_Vector = (vector unsigned char)(4,5,6,7,12,13,14,15,20,21,22,23,28,29,30,31);
vector unsigned char vcvmrgh = (vector unsigned char) (0,1,2,3,16,17,18,19,4,5,6,7,20,21,22,23);
vector unsigned char vcvmrgl = (vector unsigned char) (8,9,10,11,24,25,26,27,12,13,14,15,28,29,30,31);
/* input vectors are in interleaved form in A1,A2 and B1,B2 with each input vector representing 2 complex numbers
and thus this loop would repeat for N/4 iterations */
I1 = spu_shuffle(A1, A2, I_Perm_Vector); /* pulls out 1st and 3rd 4-byte element from vectors A1 and A2 */
I2 = spu_shuffle(B1, B2, I_Perm_Vector); /* pulls out 1st and 3rd 4-byte element from vectors B1 and B2 */
Q1 = spu_shuffle(A1, A2, Q_Perm_Vector); /* pulls out 2nd and 4th 4-byte element from vectors A1 and A2 */
Q2 = spu_shuffle(B1, B2, Q_Perm_Vector); /* pulls out 3rd and 4th 4-byte element from vectors B1 and B2 */
A1 = spu_nmsub(Q1, Q2, v_zero); /* calculates –(bd – 0) for all four elements */
A2 = spu_madd(Q1, I2, v_zero); /* calculates (bc + 0) for all four elements */
Q1 = spu_madd(I1, Q2, A2); /* calculates ad + bc for all four elements */
I1 = spu_madd(I1, I2, A1); /* calculates ac – bd for all four elements */
D1 = spu_shuffle(I1, Q1, vcvmrgh); /* spreads the results back into interleaved format */
D2 = spu_shuffle(I1, Q1, vcvmrgl); /* spreads the results back into interleaved format */

## Slide 27: Complex Multiplication – code example
Example uses an “offload” model
  ‘complexmult’ function is extraced from PPC code to SPE
Overall code uses PPC to initiate operation
  PPC code tells SPE what to do (run ‘complexmult’) via mailbox
  PPC code passes pointer to function’s arglist in main memory to SPE via mailbox
  PPC waits for SPE to finish
SPE code
  fetches arglist from main memory via DMA
  fetches input data via DMA and writes back output data via DMA
  reports completion to PPC via mailbox
SPE operations are double-buffered
  ith DMA operation is started before main loop
  (i+1)th DMA operation is started at beginning of main loop at secondary storage area
  main loop then waits on ith DMA to complete
Notice that all storage areas are 128B aligned

## Slide 28: Complex Multiplication – SPE – Blocked Inner Loop
for (jjo = 0; jjo < outerloopcount; jjo++)
{
mfc_write_tag_mask (src_mask);
mfc_read_tag_status_any ();
mfc_get ((void *) a[(jo+1)&1], (unsigned int)input1, BYTES_PER_TRANSFER, src_tag, 0, 0);
input1 += COMPLEX_ELEMENTS_PER_TRANSFER;
mfc_get ((void *) b[(jo+1)&1], (unsigned int)input2, BYTES_PER_TRANSFER, src_tag, 0, 0);
input2 += COMPLEX_ELEMENTS_PER_TRANSFER;
voutput = ((vector float *) d1[jo&1]);
vdata = ((vector float *) a[jo&1]);
vweight = ((vector float *) b[jo&1]);
ji = 0;
for (jji = 0; jji < innerloopcount; jji+=2)
{
A1 = vdata[ji];
A2 = vdata[ji+1];
B1 = vweight[ji];
B2 = vweight[ji+1];
I1 = spu_shuffle(A1, A2, I_Perm_Vector);
I2 = spu_shuffle(B1, B2, I_Perm_Vector);
Q1 = spu_shuffle(A1, A2, Q_Perm_Vector);
Q2 = spu_shuffle(B1, B2, Q_Perm_Vector);
A1 = spu_nmsub(Q1, Q2, v_zero);
A2 = spu_madd(Q1, I2, v_zero);
Q1 = spu_madd(I1, Q2, A2);
I1 = spu_madd(I1, I2, A1);
D1 = spu_shuffle(I1, Q1, vcvmrgh);
D2 = spu_shuffle(I1, Q1, vcvmrgl);
voutput[ji] = D1;
voutput[ji+1] = D2;
ji += 2;
}
mfc_write_tag_mask (dest_mask);
mfc_read_tag_status_all ();
mfc_put ((void *)d1[jo&1], (unsigned int) output, BYTES_PER_TRANSFER, dest_tag, 0, 0);
output += COMPLEX_ELEMENTS_PER_TRANSFER;
jo++;
}
wait for DMA completion for this outer loop pass
initiate DMA for next outer loop pass
execute function for DMA’d data block

## Slide 29: Links
Cell Broadband Engine resource center
  http://www-128.ibm.com/developerworks/power/cell/
CBE forum at alphaWorks
  http://www-128.ibm.com/developerworks/forums/dw_forum.jsp?forum=739&cat=46