Introduction to the Cell
(class 2)
Prof. John Dorband

---
Blade Cluster Architecture
MPI
NUMA SMP
Multi-thread
DM MIMD
SIMD

---
Cell Blade Hardware Overview
Blade
Two Cell BE Processors
1GB XDRAM
BladeCenter Interface ( Based on IBM JS20)
Chassis
Standard IBM BladeCenter form factor with:
7 Blades (for 2 slots each) with full performance
2 switches (1Gb Ethernet) with 4 external ports each
Updated Management Module Firmware.
External Infiniband Switches with optional FC ports.
Blade
Chassis
Blade
XDRAM
XDRAM
Cell
Processor
Cell
Processor
South
Bridge
South
Bridge
GbE
GbE
IB
4X
IB
4X
Typical Configuration (available today from E&TS)
eServer 25U Rack
7U Chassis with Cell BE Blades, OpenPower 710
Nortel GbE switch
GCC C/C++ (Barcelona) or XLC Compiler for Cell (alphaworks)
SDK Kit on http://www-128.ibm.com/developerworks/power/cell/
BladeCenter Network Interface

---
Cell BE Processor Can Support Many Systems
- Game console systems
- Blades
- HDTV
- Home media servers
- Supercomputers
XDRtm
XDRtm
XDRtm
XDRtm
Cell BE
Processor
Cell BE
Processor
IOIF
BIF
IOIF
XDRtm
XDRtm
XDRtm
XDRtm
XDRtm
XDRtm
Cell BE
Processor
Cell BE
Processor
IOIF
IOIF
SW
BIF
BIF
IOIF
Cell BE
Processor
IOIF
Cell BE
Processor
Cell BE
Processor
IOIF0
IOIF1
XDRtm
XDRtm
XDRtm
XDRtm
[Speaker Notes: Check for cluster configuration ... Configuration w/ switches]

---
Cell Processor
Cell Processor
25.6 GB/sec Memory Inteface
Synergistic Processor Elements (SPE):
8 per chip
128-bit wide SIMD Units
Integer and Floating Point capable
256KB Local Store
Up to 25.6 GF/s per SPE ---
        200GF/s total *
“Supercomputer-on-a-Chip”
Power Processor Element (PPE):
General Purpose, 64-bit RISC
   Processor (PowerPC 2.02)
2-Way Hardware Multithreaded
L1 : 32KB I ; 32KB D
L2 : 512KB
Coherent load/store
VMX
3.2 GHz
* At clock speed of 3.2GHz
Internal Interconnect:
Coherent ring structure
300+ GB/s total internal
  interconnect bandwidth
DMA control to/from SPEs
  supports >100 outstanding
  memory requests
20 GB/sec Coherent Interconnect
5 GB/sec I/O Bus
External Interconnects:
25.6 GB/sec BW memory interface
2 Configurable I/O Interfaces
Coherent interface (SMP)
Normal I/O interface (I/O & Graphics)
Total BW configurable between interfaces
Up to 35 GB/s out
Up to 25 GB/s in
Memory Management & Mapping
SPE Local Store aliased into PPE system memory
MFC/MMU controls SPE DMA accesses
Compatible with PowerPC Virtual Memory architecture
S/W controllable from PPE MMIO
Hardware or Software TLB management
SPE DMA access protected by MFC/MMU
Element Interconnect Bus
MFC
Local Store
SPU
N
AUC
MFC
Local Store
SPU
N
AUC
Power Core
(PPE)
L2 Cache
NCU
Local Store
SPU
MFC
N
AUC
Local Store
SPU
MFC
N
AUC
N
N
N
N
MFC
Local Store
SPU
N
AUC
MFC
Local Store
SPU
N
AUC
MFC
Local Store
SPU
N
AUC
MFC
Local Store
SPU
N
AUC

---
Cell Broadband Engine TM: A Heterogeneous Multi-core Architecture
Cell Broadband Engine TM:
A Heterogeneous Multi-core Architecture
* Cell Broadband Engine is a trademark of Sony Computer Entertainment, Inc.

---
1 PPE core:
 - VMX unit
 - 32k L1 caches
 - 512k L2 cache
 - 2 way SMT

---
8 SPEs
-128-bit SIMD instruction set
- Register file – 128x128-bit
- Local store – 256KB
- MFC
- Isolation mode

---
Cell BE Block Diagram
Cell BE Block Diagram
SPE
EIB (up to 96B/cycle)
16B/cycle
16B/cycle
PPE
MIC
BIC
L2
32B/cycle
Dual XDRTM
FlexIOTM
64-bit Power Architecture with VMX
LS
SXU
SPU
MFC
PXU
L1
PPU
16B/cycle
LS
SXU
SPU
MFC
LS
SXU
SPU
MFC
LS
SXU
SPU
MFC
LS
SXU
SPU
MFC
LS
SXU
SPU
MFC
LS
SXU
SPU
MFC
LS
SXU
SPU
MFC

---
SPE Block Diagram
SPE Block Diagram
SPU Core: Registers & Logic
Channel Unit: Message passing interface for I/O
Local Store: 256KB of SRAM private to the SPU Core
DMA Unit: Transfers data between Local Store and Main Memory
SPE
SPU
SPU Core (SXU)
Channel Unit
Local Store
MFC
(DMA Unit)
To Element Interconnect Bus

---
Register Scalar Data Layout
Register Scalar Data Layout
Preferred slot in bytes 0-3
  - By convention for procedure interfaces
  - Used by instructions expecting scalar data
    - Addresses, branch conditions, generate controls for insert

---
Per SPE Resources (SPU Side)
SPU Direct Access Resources
SPU Indirect Access Resources
    (via EA Addressed DMA)
128 - 128 bit GPRs
 External Event Status (Channel 0)
Decrementer Event
Tag Status Update Event
DMA Queue Vacancy Event
SPU Incoming Mailbox Event
Signal 1 Notification Event
Signal 2 Notification Event
Reservation Lost Event
 External Event Mask (Channel 1)
 External Event Acknowledgement (Channel 2)
 Signal Notification 1 (Channel 3)
 Signal Notificaiton 2 (Channel 4)
 Set Decrementer Count (Channel 7)
 Read Decrementer Count (Channel 8)
 16 Entry MFC Command Queue Interface (Channels 16-21)
 DMA Tag Group Query Mask (Channel 22)
 Request Tag Status Update (Channel 23)
 Immediate
Conditional - ALL
Conditional - ANY
 Read DMA Tag Group Status (Channel 24)
 DMA List Stall and Notify Tag Status (Channel 25)
 DMA List Stall and Notify Tag Acknowledgement (Channel 26)
 Lock Line Command Status (Channel 27)
 Outgoing Mailbox to PU (Channel 28)
 Incoming Mailbox from PU (Channel 29)
 Outgoing Interrupt Mailbox to PU (Channel 30)
System Memory
Memory Mapped I/O
This SPU Local Store
Other SPU Local Store
Other SPU Signal Registers
Atomic Update (Cacheable Memory)

---
Per SPE Resources (PPE Side)
Problem State
Privileged 2 State
(OS or Hypervisor)
Privileged 1 State (OS)
4K Physical Page Boundary
4K Physical Page Boundary
4K Physical Page Boundary
 8 Entry MFC Command Queue Interface
 DMA Command and Queue Status
 DMA Tag Status Query Mask
 DMA Tag Status
 32 bit Mailbox Status and Data from SPU
 32 bit Mailbox Status and Data to SPU
     4 deep FIFO
 Signal Notification 1
 Signal Notification 2
 SPU Run Control
 SPU Next Program Counter
 SPU Execution Status
 SPU Master Run Control
 SPU ID
 SPU ECC Control
 SPU ECC Status
 SPU ECC Address
 SPU 32 bit PU Interrupt Mailbox
 MFC Interrupt Mask
 MFC Interrupt Status
 MFC DMA Privileged Control
 MFC Command Error Register
 MFC Command Translation Fault Register
 MFC SDR (PT Anchor)
 MFC ACCR (Address Compare)
 MFC DSSR (DSI Status)
 MFC DAR (DSI Address)
 MFC LPID (logical partition ID)
 MFC TLB Management Registers
 SPU Privileged Control
 SPU Channel Counter Initialize
 SPU Channel Data Initialize
 SPU Signal Notification Control
 SPU Decrementer Status & Control
 MFC DMA Control
 MFC Context Save / Restore Registers
 SLB Management Registers
4K Physical Page Boundary
4K Physical Page Boundary
 Optionally Mapped 256K Local Store
 Optionally Mapped 256K Local Store

---
Memory Flow Controller Commands
DMA Commands
Put - Transfer from Local Store to EA space
Puts - Transfer and Start SPU execution
Putr - Put Result - (Arch. Scarf into L2)
Putl - Put using DMA List in Local Store
Putrl - Put Result using DMA List in LS (Arch)
Get - Transfer from EA Space to Local Store
Gets - Transfer and Start SPU execution
Getl - Get using DMA List in Local Store
Sndsig - Send Signal to SPU
Command Modifiers: <f,b>
f: Embedded Tag Specific Fence
Command will not start until all previous commands
in same tag group have completed
b: Embedded Tag Specific Barrier
Command and all subsiquent commands in same
tag group will not start until previous commands in same
tag group have completed
Command Parameters
LSA - Local Store Address (32 bit)
  EA - Effective Address (32 or 64 bit)
  TS - Transfer Size (16 bytes to 16K bytes)
  LS - DMA List Size (8 bytes to 16 K bytes)
  TG - Tag Group(5 bit)
  CL - Cache Management / Bandwidth Class
Synchronization Commands
Lockline (Atomic Update) Commands:
getllar - DMA 128 bytes from EA to LS and set Reservation
putllc - Conditionally DMA 128 bytes from LS to EA
putlluc - Unconditionally DMA 128 bytes from LS to EA
barrier - all previous commands complete before subsiquent
commands are started
mfcsync - Results of all previous commands in Tag group
are remotely visible
mfceieio - Results of all preceding Puts commands in same
group visible with respect to succeeding Get commands
SL1 Cache Management Commands
sdcrt - Data cache region touch (DMA Get hint)
sdcrtst - Data cache region touch for store (DMA Put hint)
sdcrz - Data cache region zero
sdcrs - Data cache region store
sdcrf - Data cache region flush

---
Element Interconnect Bus
Element Interconnect Bus

---
System Memory Interface:
- 16 B/cycle
- 25.6 GB/s (1.6 Ghz)

---
MFC Detail
MFC Detail
Memory Flow Control System
DMA Unit
LS <-> LS, LS<-> Sys Memory, LS<-> I/O Transfers
8 PPE-side Command Queue entries
16 SPU-side Command Queue entries
MMU similar to PowerPC MMU
8 SLBs, 256 TLBs
4K, 64K, 1M, 16M page sizes
Software/HW page table walk
PT/SLB misses interrupt PPE
Atomic Cache Facility
4 cache lines for atomic updates
2 cache lines for cast out/MMU reload
Up to 16 outstanding DMA requests in BIU
Resource / Bandwidth Management Tables
Token Based Bus Access Management
TLB Locking
Isolation Mode Support (Security Feature)
Hardware enforced “isolation”
SPU and Local Store not visible (bus or jtag)
Small LS “untrusted area” for communication area
Secure Boot
Chip Specific Key
Decrypt/Authenticate Boot code
“Secure Vault” – Runtime Isolation Support
Isolate Load Feature
Isolate Exit Feature

---
Element Interconnect Bus (EIB)
- 96B / cycle bandwidth

---
Internal Bandwidth Capability
Internal Bandwidth Capability
- EIB data ring for internal communication
  - Four 16 byte data rings, supporting multiple transfers
  - 96B/cycle peak bandwidth
  - Over 100 outstanding requests
- Each EIB Bus data port supports 25.6GBytes/sec* in each direction
- The EIB Command Bus streams commands fast enough to support 102.4 GB/sec for coherent commands, and 204.8 GB/sec for non-coherent commands.
- The EIB data rings can sustain 204.8GB/sec for certain workloads, with transient rates as high as 307.2GB/sec between bus units
* The above numbers assume a 3.2GHz core frequency – internal bandwidth scales with core frequency

---
Element Interconnect Bus - Data Topology
Element Interconnect Bus - Data Topology
Four 16B data rings connecting 12 bus elements
  - Two clockwise / Two counter-clockwise
- Physically overlaps all processor elements
- Central arbiter supports up to three concurrent transfers per data ring
  - Two stage, dual round robin arbiter
Each element port simultaneously supports 16B in and 16B out data path
  - Ring topology is transparent to element data interface
SPE1
SPE3
SPE5
SPE7
PPE
IOIF1
16B
16B
16B
16B
16B
16B
16B
16B
16B
16B
16B
16B
Data Arb
16B
16B
16B
16B
16B
16B
16B
16B
16B
16B
16B
16B
BIF/IOIF0
SPE6
MIC
SPE0
SPE2
SPE4
[Speaker Notes: Central arbiter supports up to three concurrent transfers per data ring Two stage, dual round robin arbiter]

---
Example of eight concurrent transactions
Example of eight concurrent transactions
Ramp
7
Controller
Ramp
8
Controller
Ramp
9
Controller
Ramp
10
Controller
Ramp
11
Controller
Data
Arbiter
Ramp
7
Controller
Ramp
8
Controller
Ramp
9
Controller
Ramp
10
Controller
Ramp
11
Controller
Controller
Controller
Controller
Controller
Controller
Controller
Ramp
5
Ramp
4
Ramp
3
Ramp
2
Ramp
1
Ramp
0
IOIF0
Ring1
Ring0
controls
Ring3
Ring2
MIC
SPE0
SPE2
SPE4
SPE6
BIF /
IOIF1
Controller
Ramp
0
Controller
Ramp
1
Controller
Ramp
2
Controller
Ramp
3
Controller
Ramp
4
Controller
Ramp
5
Controller
Ramp
6
Controller
Ramp
7
Controller
Ramp
8
Controller
Ramp
9
Controller
Ramp
10
Controller
Ramp
11
PPE
SPE1
SPE3
SPE5
SPE7
IOIF1
PPE
SPE1
SPE3
SPE5
SPE7
IOIF1
PPE
SPE1
SPE3
SPE5
SPE7
IOIF1
MIC
SPE0
SPE2
SPE4
SPE6
BIF /

---
I/O and Memory Interfaces
I/O and Memory Interfaces

---
I/O Interface:
- 16 B/cycle x 2

---
I/O and Memory Interfaces
- I/O Provides wide bandwidth
  - Dual XDRTM controller (25.6GB/s @ 3.2Gbps)
  - Two configurable interfaces (76.8GB/s @6.4Gbps)
    - Configurable number of Bytes
    - Coherent or I/O Protection
  - Allows for multiple system configurations